## Slide 1: ATHENA: The Advanced Telescope for High Energy Astrophysics
Nicholas E. White, NASA/GSFC
On behalf of the Athena Study Team
Revealing the Extreme Universe from Black Holes to Large Scale Structure

## Slide 2: New L-class boundary conditions
Programmatic assumptions:
ESA-led mission with ESA Cost at Completion < 850 MЄ
International cooperation: low-level contributions from JAXA and NASA.
Instruments procured by ESA members states (< 200 M Є) and/or partner agencies (e.g. JAXA and NASA).
TRL ≥ 5 by early 2014 (by end of Phase A).
Targeting launch opportunity by end of 2022.
Implementation phase < 7 yr (including contingency).
Mission schedule milestones:
Following SPC decision (Feb 2012), mission entering directly the Definition Phase (A/B1), with system level studies starting in Q3/2012 (TBC).
Instruments AO released in Q1/2013.
Final missions selection in Q2/2014 (at the end of phase A).
Completion of Phase B1 by end 2014.
Implementation phase (B2/C/D) KO in Q1/2015.

## Slide 3: The Reformulation Process
The Problem:
  Fit within ESA cost of <850M€ while retaining key science
Solution:
  Lower Mass (Lower Mirror Effective Area)
  Reduced Complexity (e.g. EOB, Mechanisms)
  Fewer Instruments (6 to 2)
Tradeoff:
  Which Instruments? (XMS, WFI)
  1, 2 or 3 telescopes (1 keV vs 6 keV science)
Process:
  11 Scientific “Task Teams” set up to investigate science potential and impact of tradeoffs
  Broad involvement (100+ scientists), very short timescale
  Presentations and discussion at ESTEC 28th April
  Science Team Meeting at MPE June 14-15

## Slide 4: Athena Implementation
Focal plane
MA
Mirror Assembly
Service Module
Fixed OB
11.5m Focal length
ESA Silicon Pore Optics
Ariane V launch to L2
5yr nominal mission
Two telescope with 10” resolution (5” goal) with single fixed instrument at each focal plane

## Slide 5: Two Athena Instruments
FPA
FMS
MA
SVM
Wide Field Imager (WFI)
25 x 25 arc min FOV
150 eV @ 6 keV
Microcalorimeter (XMS)
2.4 x 2.4 arc min FOV
3 eV @ 6 KeV
JAXA, NASA contributions

## Slide 6
Figure of Merit: Spectroscopy

## Slide 7: Figure of Merit: Imaging Sensitivity
confusion
At 1Ms with 10” resolution, the sensitivity of ~4 10-17 is comparable with confusion limit
Power law AGN at high latitude
L* AGN @ Z~6

## Slide 8: Athena Science Objectives
Diagnose hot cosmic plasmas on all astrophysical environments via spatially resolved high resolution X-ray spectroscopy

## Slide 9: Athena Science Requirements
Effective Area | 1 m2 @1.25 keV (goal 1.2 m2) 0. 5 m2 @ 6 keV (goal 0.7 m2) | Black hole evolution, large scale structure Strong gravity, cosmic feedback
Spectral Resolution (FWHM) | ΔE = 3 eV (@6keV) within 2 x 2 arc min (goal 2.5 eV and 4x3 arc min) ΔE =150 eV at 6 keV within 25 arc min diam (goal of 125 eV and >30 arc min) | Large scale structure, Cosmic Feedback Black Hole evolution, Large scale structure
Angular Resolution | 10 arc sec HPD (0.1 – 7 keV) (goal of 5 arc sec) | Black hole evolution, Cosmic feedback, Large Scale Structure
Count Rate | 1 Crab with >90% throughput. ΔE < 200 eV @ 6keV (0.3 – 15 keV) | Strong gravity
Astrometry | 1.5 arcsec at 3σ confidence | Black hole evolution
Absolute Timing | 100 μsec | Compact Objects

## Slide 10
Black Holes and Accretion Physics
AGN, BHB, NS binaries, Sgr A*, ULX, CVs etc.
M. Cappi, C. Reynolds, L. Brenneman

## Slide 11
Cosmic Evolution of SMBH
Compton thick
AGN@z~2
Fe Ka
A. Comastri
AGN census at z>6? goal PSF (5”) and WFI FOV (>30’)

## Slide 12
The Physics of Feedback
AGN feedback via outflows
A. Fabian, J. Sanders

## Slide 13
Large-Scale Structure
WFI: group, clusters census to z>2
XMS: baryon physics, mass proxies
Clusters
 COSMOLOGY
Missing Baryons/WHIM
J. De Plaa
L. Piro

## Slide 14: Astrophysics of hot cosmic plasmas
Charge exchange in Solar System bodies: planetary atmospheres, comets, etc.
Stellar evolution:
Young Stellar Objects
Cool stars
Massive stars, mass loss, magnetic fields, etc.
Supernovae and Supernova remnants
Winds and absorption studies in X-ray binaries
Cataclysmic variables
X-ray binary populations in external galaxies
The ISM of our galaxy
And many many more….

## Slide 15: ATHENA: The Next Steps
 | Jul | Aug | Sep | Oct | Nov | Dec | Jan | Feb
Industry Study |  |  |  |  |  |  |  | 
ESTEC Review |  |  |  |  |  |  |  | 
AWG Review |  |  |  |  |  |  |  | 
JAXA MDR |  |  |  |  |  |  |  | 
Document Pack
Yellow Book
SPC Decision

## Slide 16: Possible NASA Contributions
The following are being discussed:
Instrument contributions
  XMS: A TES array and readout electronics, as well as a 3 stage ADR
  WFI: Electronics and software
Infrastructure contributions
  Use of the X-ray Calibration Facility at MSFC
Support for US Guest Observers similar to that for Herschel and XMM-Newton
  Contributions to data analysis software

## Slide 17: Process for Selecting NASA Participation
Current thinking is to fund NASA participation through the Explorer program via a Mission of Opportunity call on a TBD timeframe that will ultimately align with the ESA instrument AO process